## Slide 1
Adaptive Cache Partitioning on a Composite Core
Jiecao Yu, Andrew Lukefahr, Shruti Padmanabha,
Reetuparna Das, Scott Mahlke
Computer Engineering Lab
University of Michigan, Ann Arbor
June 14th, 2015

## Slide 2
Energy Consumption on Mobile Platform
Chart: Normalized CPU Power Consumption
| Nexus One | Nexus S | Galaxy Nexus | Nexus 4 | Nexus 5 | Nexus 6
CPU Power Consumption | 1 | 1.6902 | 3.7557 | 6.6639 | 4.918 | 6.3934
Battery | 1 | 1.0714 | 1.25 | 1.5 | 1.6429 | 2.3

## Slide 3
Multiple cores with different implementations
Heterogeneous Multicore System (Kumar, MICRO’03)
ARM big.LITTLE
Applications migration
  Mapped to the most energy-efficient core
  Migrate between cores
  High overhead
Instruction phase must be long
  100M-500M instructions
Fine-grained phases expose opportunities
Reduce migration overhead
Composite Core

## Slide 4
Primary Thread
Composite Core (Lukefahr, MICRO’12)
Big μEngine
Shared Front-end
Shared L1 Caches
Secondary Thread
Little μEngine
  - 0.5x performance
  - 5x less power

## Slide 5
Problem with Cache Contention
Threads compete for cache resources
  L2 cache space in traditional multicore system
  Memory intensive threads get most space
  Decrease total throughput
L1 cache contention – Composite Cores / SMT
Foreground
Background

## Slide 6
Chart: 
| astar-astar* | gcc-gcc* | gobmk-gobmk | h264ref-h264ref | omnetpp-omnetpp* | sjeng-sjeng | xalancbmk-xalancbmk | xalancbmk-hmmer | xalancbmk-gcc | mcf-mcf* | gcc-bzip2 | gcc-hmmer | gcc-sjeng | mcf-astar | mcf-hmmer | gobmk-xalancbmk | libquantum-sjeng | mcf-perlbench | geomean
Exclusive Data Cache (Primary) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Shared Data Cache | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Performance Loss of Primary Thread
Worst case: 28% decrease
Average: 10% decrease
Normalized IPC
Chart: 
| astar-astar* | gcc-gcc* | gobmk-gobmk | h264ref-h264ref | omnetpp-omnetpp* | sjeng-sjeng | xalancbmk-xalancbmk | xalancbmk-hmmer | xalancbmk-gcc | mcf-mcf* | gcc-bzip2 | gcc-hmmer | gcc-sjeng | mcf-astar | mcf-hmmer | gobmk-xalancbmk | libquantum-sjeng | mcf-perlbench | geomean
Exclusive Data Cache (Primary) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Shared Data Cache | 0.97398 | 0.88857 | 0.93695 | 0.9751 | 0.81338 | 0.95462 | 0.80807 | 0.89788 | 0.82244 | 0.89164 | 0.97226 | 0.94557 | 0.96168 | 0.8999 | 0.94584 | 0.86237 | 0.99739 | 0.71151 | 0.90011

## Slide 7
Solutions to L1 Cache Contention
All data cache to the primary thread
  Naïve solution
  Performance loss on secondary thread
Cache Partitioning
  Resolve cache contention
  Maximize the total throughput

## Slide 8
Existing Cache Partitioning Schemes
Existing Schemes
  Placement-based e.g., molecular caches (Varadarajan, MICRO’06)
  Replacement-based e.g., PriSM (Manikantan, ISCA’12)
Limitations
  Focus on last level cache
  High overhead
  No limitation on primary thread performance loss
L1 caches + Composite Cores

## Slide 9
Adaptive Cache Partitioning Scheme
Limitation on primary thread performance loss
  Maximize total throughput
Way-partitioning and augmented LRU policy
  Structural limitations of L1 caches
  Low overhead
Adaptive scheme for inherent heterogeneity
  Composite Core
Dynamic resizing at a fine granularity

## Slide 10
Augmented LRU Policy
Set Index
Cache Access
Miss!
LRU Victim!
Primary
Primary
Secondary

## Slide 11
L1 Caches of a Composite Core
Limitation of L1 caches
  Hit latency
  Low associativity
Smaller size than most working sets
  Fine-grained memory sets of instruction phases
Heterogeneous memory access
  Inherent heterogeneity
  Different thread priorities

## Slide 12
Adaptive Scheme
Cache partitioning priority
  Cache reuse rate
  Size of memory sets
Cache space resizing based on priorities
  Raising priority (↑)
  Lower priority (↓)
  Maintain priority ( = )
Primary thread tends to get higher priority

## Slide 13
Case – Contention
gcc* - gcc*
Memory sets overlap
High cache reuse rate + small memory set
Both threads maintain priorities
Overlap
+
+
+
+
Time
Set Index in Data Cache

## Slide 14
Evaluation
Multiprogrammed workload
  Benchmark1 – Benchmark2 (Primary – Secondary)
95% performance limitation
  Baseline: primary thread with all data cache
Oracle simulation
  Length of instruction phases: 100K instructions
  Switching disabled / only data cache
  Runs under six cache partitioning modes
  Mode maximizing the total throughput under the limitation of primary thread performance

## Slide 15
Cache Partitioning Modes
Mode 0
Mode 1
Mode 2
Mode 3
Mode 4
Mode 5

## Slide 16
Architecture Parameters
Architectural Features | Parameters
Big μEngine | 3 wide Out-of-Order @ 2.0GHz 12 stage pipeline 92 ROB Entries 144 entry register file
Little μEngine | 2 wide In-Order @ 2.0GHz 8 stage pipeline 32 entry register file
Memory System | 32 KB L1 I – Cache 64 KB L1 D – Cache 1MB L2 cache, 18 cycle access 4GB Main Mem, 80 cycle access

## Slide 17
Chart: 
| astar-astar* | gcc-gcc* | gobmk-gobmk | h264ref-h264ref | omnetpp-omnetpp* | sjeng-sjeng | xalancbmk-xalancbmk | xalancbmk-hmmer | xalancbmk-gcc | mcf-mcf* | gcc-bzip2 | gcc-hmmer | gcc-sjeng | mcf-astar | mcf-hmmer | gobmk-xalancbmk | libquantum-sjeng | mcf-perlbench | geomean
No Perf. Loss | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Shared Data Cache | 0.97398 | 0.88857 | 0.93695 | 0.9751 | 0.81338 | 0.95462 | 0.80807 | 0.89788 | 0.82244 | 0.89164 | 0.97226 | 0.94557 | 0.96168 | 0.8999 | 0.94584 | 0.86237 | 0.99739 | 0.71151 | 0.90011
Adaptive Scheme | 0.97752 | 0.95008 | 0.94998 | 0.97553 | 0.94978 | 0.95723 | 1.0008 | 0.94985 | 0.99948 | 0.95002 | 0.97439 | 0.95014 | 0.96202 | 0.94889 | 0.94995 | 0.99641 | 1 | 0.96385 | 0.96681
Performance Loss of Primary Thread
<5% for all workloads, 3% on average
Normalized IPC

## Slide 18
Total Throughput
Normalized IPC
Limitation on primary thread performance loss
Sacrifice Total Throughput but Not Much
Chart: 
| astar-astar* | gcc-gcc* | gobmk-gobmk | h264ref-h264ref | omnetpp-omnetpp* | sjeng-sjeng | xalancbmk-xalancbmk | xalancbmk-hmmer | xalancbmk-gcc | mcf-mcf* | gcc-bzip2 | gcc-hmmer | gcc-sjeng | mcf-astar | mcf-hmmer | gobmk-xalancbmk | libquantum-sjeng | mcf-perlbench | geomean
No Perf. Loss | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Shared Data Cache | 1.6924 | 1.3298 | 1.2291 | 1.2641 | 1.038 | 1.2794 | 0.98382 | 1.6041 | 0.99836 | 1.0041 | 1.6403 | 1.7155 | 1.5273 | 1.4198 | 2.0269 | 1.0347 | 1.3194 | 1.0347 | 1.3096
Adaptive Scheme | 1.6982 | 1.1128 | 1.182 | 1.262 | 0.99117 | 1.2808 | 1.0009 | 1.1082 | 0.99957 | 1.009 | 1.643 | 1.6608 | 1.5302 | 1.1179 | 1.837 | 0.99956 | 1.3214 | 1.0347 | 1.2384

## Slide 19
Conclusion
Adaptive cache partitioning scheme
  Way-partitioning and augmented LRU policy
  L1 caches
  Composite Core
  Cache partitioning priorities
Limitation on primary thread performance loss
  Sacrifice total throughput
Questions?

## Slide 20
Adaptive Cache Partitioning on a Composite Core
Jiecao Yu, Andrew Lukefahr, Shruti Padmanabha,
Reetuparna Das, Scott Mahlke
Computer Engineering Lab
University of Michigan, Ann Arbor
June 14th, 2015